## Slide 1
Mem-Side Local
Only L2
(b) Static R$
(c) Shared Coherent L1+L2
(d) NUMA-Aware L1+L2
0) Allocate ½ ways for local and ½ for remote data
Estimate incoming inter-GPU BW and monitor local outgoing DRAM BW
If inter-GPU BW is saturated and DRAM BW not
- RemoteWays++ and LocalWays--
If DRAM BW is saturated and inter-GPU BW not
- RemoteWays-- and LocalWays++
If both are saturated
- Equalize allocated ways (++ and --)
None of them is saturated
- Do nothing
Go back to 1) after SampleTime cycles
Cache Partitioning Algorithm
SW-based
Coherent
To Switch
SM
…
L1
SM
L1
NoC
L2
DRAM
…
R$
Not
Coherent
SW-based
Coherent
To Switch
SM
…
L1
SM
L1
NoC
L2
DRAM
…
Not
Coherent
SW-based
Coherent
To Switch
SM
…
L1
SM
L1
NoC
DRAM
…
Coherent L2
SW-based
Coherent
To Switch
SM
…
L1
SM
L1
NoC
DRAM
…
Coherent L2